## Slide 1
Group member :
1)Husna bt Abdul Halim
2)Idham bin Daub
3)Lai Sinhan
4)Lieu Hin Ming
5)Lim Yee Yern
6)Megat Muhammad Daniel Bin Syahriman Effende
7)Mohamad Faris Ifran Bin Mohd Adib
8)Mohamad Iqbal Bin Mohd Zulkifli
9)Mohammad Hanif Bin Yaakub
10)Myhammad Farris Bin Kamal
11)Mugannad Ridza Ikmal Bin Zakaria
Soil Presentation

## Slide 2: Soil Classification
Soil classification require to condition where :
-meaningful to user
-parameters easy to measure quantitatively.
-imply simple engineering properties.
Coarse-grained soil
-large particles
-can be seen with naked eyes
Fine-grained soil (silts and clay and have particles smaller than 60µm
Simple test to classify and identify soil
Visual and ‘Feel’
Gravel(>2mm)
Sand (0.06mm<d<2mm)
Silts (0.02mm<d<0.06mm)
Clays (<0.002mm)
Grading
-refer to distribution
-Well graded/poorly graded or uniform soil.
Compactness
Estimated using hand spade or pick or driving in small wooden peg.
Cohesion, plasticity and consistency
-depend on moisture content
-can be easily moulded.
Laboratory test
Particle size :
-def : particles size varies from 200mm to clays less than 0.001 mm.
-Sieve analysis test
-sendimentation analysis test
Atterberg’s Limits ( PI=LL-PL)
-liquid limit test
-plastic limit test

## Slide 3: Soil Classification
Unified Soil Classification System (USCS)
American Association of State Highway and Transportation Officials (AASHTO) System
Step 1: Read the percentage passing through sieve No. 200.
<35%
>35%
A-1
A-2
Read sieve No.10 and 40
Read LL and PI
A-4 to A-6
Read LL and PI
A-7
Read LL and PI
Compare value of PI and LL-30
Step 1: Determine % of soil passing No.200 sieve (F)
If F<50%, it is coarse-grained soil
If F>50%, it is fine-grained soil
Step2: Determine the % of coarse fraction passes / retained on No.4 sieve
More than 50% of soil passes No.4 sieve, then it is sands.
50% or more retained on No.4 sieve, then it is gravels.
Step 2: Refer the Plasticity Chart
Step 2: Refer Classification Criteria to know the group symbols of soil
By using LL and PI to know the group symbol of soil