FACULTY OF PETROLEUM AND RENEWABLE ENERGY ENGINEERING

TEST I

2014/2015 SEM II

SUBJECT		: 	CHEM. ENG. COMPUTATION

CODE		: 	SKKK 2123

TIME		: 	9.00 – 10.30 A.M. (1.5 HOURS)

DATE		: 	16 APRIL 2015

INSTRUCTION

- Answer all questions

- Closed book and notes test

- Switch off your handphone

- Formula is given in page 5

Question 1 (32 Marks)

Given

- Use bisection method to solve this function. Employ initial guesses of xl = 0 and xu = 1, and perform iterations until the approximate relative error falls below 5%. 											(15 marks)

- Determine the approximate relative error after each iteration and summarize your result in a table form 							(15 marks)

| iteration | xl | xu | xr | f(xl) | f(xr) | f(xl) x f(xr) | ׀εa׀ |
| --- | --- | --- | --- | --- | --- | --- | --- |

- Check your final answer by substituting the final root into the original function.											(2 marks)

(Show all the working calculation. All computation should be in 4 decimal points)

Question 2 ( 35 Marks)

You are designing a spherical tank (Figure A) to hold water for a small village in Kelantan. The volume of liquid it can hold can be computed as

where V = volume (m3), h = depth of water in tank (m), and R = the tank radius (m).

Figure A

- If the tank radius is 3 m, what depth must the tank be filled to so that it holds a volume of 30 m3? Use three iterations of the Newton-Raphson method and employ initial guess of xo=0 to determine your answer. 				(10 marks)

- Determine the approximate relative error after each iteration and tabulated your result in a table form 							(20 marks)

| iteration | xi | f(xi) | f’(xi) | ׀εa׀ |
| --- | --- | --- | --- | --- |

- Develop a MATHLAB program which can be written in a command window to solve this problem using Newton-Raphson method.				(5 marks)

(Show all the working calculation. All computation should be in 4 decimal points)

Question 3 ( 33 Marks)

A liquid-liquid extraction process conducted in the Electrochemical Materials Laboratory involved the extraction of nickel from the aqueous phase into an organic phase. A typical set of data from the laboratory is tabulated in Table A.

Table A

| Ni aqueous phase, a (g/l) | 2 | 2.5 | 3 |
| --- | --- | --- | --- |
| Ni organic phase, g (g/l) | 8.57 | 10 | 12 |

Assuming g is the amount of Ni in the organic phase and a is the amount of Ni in the aqueous phase, the quadratic interpolation that estimates g is given by

g = x1a2 + x2a + x3		2 < a < 3

The solution for then unknown x1, x2 and x3 is given by

- Find the value of  x1, x2 and x3 by using LU decomposition (Dolittle)	[25 marks]

- Estimate the amount of nickel in the organic phase when 2.3 g/l in the aqueous phase using quadratic interpolation.					[8 marks]

(Show all the working calculation. All computation should be in 4 decimal points)

FORMULA

Bisection method

Xr = (xl  + xu)/2

a) if f(xl)f(xr)<0, the root lies in the lower subinterval. Therefore, set xu = xr

b) if f(xl)f(xr)>0, the root lies in the upper subinterval. Therefore, set xl=xr

c) if f(xl)f(xr)=0, the root equal xr; terminate the computation.

Newton- Raphson

xi+1 = xi –  f(xi)

f’(xi)

LU Decomposition

[A] = [L][U] =

# Text boxes

=

x1

x2

x3

4           2         1

6.25    2.5      1

9           3        1

8.57

10

12

1          0       0

l21        1       0

l31        l32     1

u11      u12       u13

0          u22      u23

0          0          u33